## Slide 1: CellProfiler
June 14, 2024

## Slide 2: Overview
CellProfiler Operates on Objects
  Primary objects are easily segmentable objects we start with
  Secondary objects grow from Primary objects
  Tertiary objects are the subtraction of primary objects from secondary objects
  Objects are masks over any channel
  Almost all measurements are done on objects

## Slide 3: Usage tips
The easiest way to use CellProfiler is in GUI form, with all your images separated.
It is harder to work with image stacks, or hyperstacks.
  Separate z-stacks into image sequences
  Separate time-series out as well.
CellProfiler isn’t easy to use in 4D.

## Slide 4: Usage tips
The easiest way to use CellProfiler is in GUI form, with all your images separated.
It is harder to work with image stacks, or hyperstacks.
  Separate z-stacks into image sequences
  Separate time-series out as well.
CellProfiler isn’t easy to use in 4D.

## Slide 5: Loading Images
Drop files into the dialog box here

## Slide 6: Image Naming
Use rules to differentiate between images
Make sure that each channel has a unique identifier
Usually use the rules ‘Does’ or ‘Does not’ contain an expression. Avoid regular expressions.
Click update and make sure that everything is lined up properly
Numbering goes :
1,10,11,12,….19,2,20,21…….29,3,30…
Always number files 01,02, 03….10,11. etc.
If you will have more than a hundred images
001, 002, 003, ….010….099, 100;

## Slide 7: Task 1
Start up CellProfiler
Drag files from Improper_Broad_Cells/Bad_Wrong_int_split into the files box.
Input the images into CellProfiler and create rules to differentiate the images
C1 = Tubulin, C2 = Cytoplasm, C3 = DAPI
  Click update…what happens?
Lots of mistakes can be made.
  Doubling (IM_01, IM_01a, IM_01_good)
  Mixed channels (sometimes, GFP is channel 1, sometimes channel 2)
  Bad integers, IM_1, IM)2….IM_10

## Slide 8: Task 2
Clear the old images out of CellProfiler file loading module
In Broad Cells folder, open up the “path\to\CellProfiler_Course_Student_Files\Broad_Cells\images” images and use split channels macro from FIJI to split the channels and save in a new folder
Input the new output images into CellProfiler and use your previously created rules to differentiate the images, and click update

## Slide 9: Objects
CellProfiler is a powerful segmentation tool. The result of segmentation are objects, which are the backbone of all subsequent processing.
  Objects can be extended to find secondary or tertiary objects
  Objects can be measured over multiple channels (i.e. use a nuclear object as a mask to measure the signal of another channel inside nuclei).
  Objects can be merged, split, eroded, filtered by measurements
  Objects can be tracked

## Slide 10: Primary Objects
Primary objects are those that are found from an image without any additional information.
Easily detectable objects, as opposed to confluent cells.
Can be found by image analysis techniques in CellProfiler
  Thresholding, watershed, etc.
Can be imported from outside image segmentation
  StarDist, Cellpose
IdentifyPrimaryObjects identifies biological objects of interest. It requires grayscale images containing bright objects on a dark background. Incoming images must be 2D (including 2D slices of 3D images); please use the Watershed module for identification of objects in 3D.

## Slide 11: Primary Objects
Primary objects are those that are found from an image without any additional information.
Easily detectable objects, as opposed to confluent cells.
Can be found by image analysis techniques in CellProfiler
  Thresholding, watershed, etc.
Can be imported from outside image segmentation
  StarDist, Cellpose
IdentifyPrimaryObjects identifies biological objects of interest. It requires grayscale images containing bright objects on a dark background. Incoming images must be 2D (including 2D slices of 3D images); please use the Watershed module for identification of objects in 3D.

## Slide 12: Thresholding
Global is more useful. If doing adaptive, then do illumination correction
Play with the thresholding method. The Otsu method lets you do a three class thresholding.
Declumping by intensity is useful if there is good demarcation between objects
Declumping by shape is useful if there is curvature between the objects

## Slide 13: Task 3
Find Primary objects in the DAPI channel
  Configure the thresholding and size so that you find whole nuclei
To test a pipeline, click ‘Start Test Mode’ and then step through it.
  Clicking on the eyeball suppresses screen output from a module
  Clicking on a check box turns on/off module
  Clicking on the pause button puts a break point in a pipeline, and you can then click ‘run’ to go as far as the breakpoint
  Changing a module, then re-clicking the green arrow will refresh the changes

## Slide 14: Secondary Objects
Secondary objects use a primary object for reference in detection, i.e. a nuclei to start, and then propogate out to find cell boundary in cytoplasm
Tertiary objects are just secondary objects with the primary object removed (i.e. cytoplasm without the nuclei)

## Slide 15: Relating Objects
Relating objects gives a child-parent relationship between two sets of objects.
This would be for something akin to RNAScope, where you would want to count the number or intensity of labelled RNA inside a nucleus

## Slide 16: Relating Objects vs Secondary Objects
Secondary objects ‘grow’ from primary objects
Related objects are ‘inside’ other objects.
  The two related objects can both be primary objects.
  You can’t relate a secondary object set to the primary object set it grew from

## Slide 17: Object Measurements
You can measure a variety of parameters of the objects
  Intensity
    Total
    Gradients
  Colocalization
  Granularity
  Texture
  Size/Shape properties
    Area
    Eccentricity
  Number of Neighbors
You can plot within CellProfiler, but you can’t save the plots programmatically.

## Slide 18: Saving Data
Can export image files and csv files
Can also export databases for CellProfiler Analyst, which is beyond the scope of this class

## Slide 19: Task 4
For this task, we’re carrying on with the broad cells
Measure the size of the primary objects (look in the list for something along the lines of ‘MeasureObjectSizeShape’
Save a csv file with the object sizes
Save your pipeline

## Slide 20: Task 5
Save your current pipeline
Open the pipeline for Example Speckles and load the data
We’re going to explore this together

## Slide 21: Coffee Break

## Slide 22: StarDist (or CellPose)
StarDist is a plugin for FIJI that allows for quick segmentation of star-convex objects (round, nuclear shaped things).
StarDist can’t be run inside CellProfiler, but it’s a great trick to know
Running StarDist on a DAPI channel, and bringing those results in to CellProfiler as a separate image channel allows for easy nuclear segmentation
Stardist can only detect objects that are Star-convex: all the points of the perimeter can be reached by rays emanating from a point somewhere in the object.

## Slide 23: StarDist in FIJI
Need to add the CSBDeep and StarDist libraries
Run stardist on a nuclear image, and save the resulting prediction image as a tiff. The ‘pixel intensity’ of each nuclei is the nuclear ID label

## Slide 24: Using StarDist
We can creat StarDist images using the FIJI plugin, or the FIJI macro we have: ‘stardist_process_folder.ijm’
StarDist label images have to be imported into CellProfiler differently:
  Use the module ConvertImageToObjects
    Convert to Boolean == no
    Preserve original labels == yes

## Slide 25: Task 6
Use StarDist to try to better differentiate the nuclei in the ExampleHuman project
Load the Example Human Pipeline
  \CellProfiler_Course_Student_Files\ExampleHuman\ExampleHuman\
Run the DAPI channel on StarDist in FIJI
Compare nuclear segmentation from the original project with that from stardist labels

## Slide 26: Task 7
  \CellProfiler_Course_Student_Files\Broad_Cells\Split_Channels
  Create the naming rules to find the Tubulin, Cytoplasm, DAPI and StarDist channels
Make an image of the StarDist nuclei overlaid on the DAPI image, and save
  You may want to play with the opacity
Measure the area of the StarDist nuclei, and display their size on a DAPI image overlay, in green
Display the outlines of the extranuclear tubulin on the DAPI image, in red
Measure the intensity of the tubulin both in and out of the nuclei.

## Slide 27: Further Study
I’ve included a 3D FISH analysis pipeline, and a 3D cell segmentation pipeline.
I’ve included a pipeline for illumination correction and a document on it. Illumination correction is often useful, especially on widefield or TIRF images, but needs understanding
You can run CellProfiler command line only, and run it distributed on and HPC cluster. This is very useful, but beyond the scope of this course. If you would like to do it, email me.

## Slide 28: Thanks
Todd Fallesen
Camille Charoy
Dan Gunton